CASPA Documentation:
Cellular Automaton for SnowPack Albedo

A coupled cellular automaton and radiative transfer model for predicting the albedo of a snowpack with biotic and abiotic impurities capable of accounting for variations in three spatial dimensions and over time.

Code and Data Availability

The code, including the driver routines and all dependencies are provided in the github repository github.com/jmcook1186/CASPA.

Authorship and Copyright

All material in the repository and this document were written by J Cook. The repository is managed and maintained by J Cook. Any correspondence should be directed to joe.cook@sheffield.ac.uk. All material contained in this document and any other items in the main repository is provided free of charge and without restriction for educational or personal use but without warranty or guarantee of any kind. The author would appreciate a citation in papers using this code, and opportunities for collaboration are welcomed.

Contents:

1. Overview

2. Cellular Automaton

2.1 Initial Conditions and update rules
2.2 Physical Tractability
2.3 Edge Effects

3. BioSNICAR
3.1 Principles of SNICAR two stream radiative transfer
3.2 Impurities
3.3 Algal cells

4. Snow Optical parameters
4.1 Grain size
4.2 Snow density
4.3 Layer thickness
4.4 Water
4.5 Illumination conditions

5. Biological parameters
5.1 Pigmentation
5.2 Cell size
5.3 Biomass
5.4 Position in snowpack
5.5 Mie optical parameters

6. Accessing and updating the BioSNICAR impurity library
6.1 NetCDF File structure
6.2 Interfacing with BioSNICAR
6.3 Updating the impurity library
6.4 Updating BioSNICAR to read new impurities

7 Biomass Development, Albedo Radiative Forcing Calculations
7.1 Biomass calculations
7.2 Spectral and Broadband Albedo
7.1 Radiative Forcing: Spectral differencing
7.2 Radiative forcing: Heating rates and temperature gradients from SNICAR

8. Snow grain evolution
8.1 Grain growth parameterisation
8.2 Incorporation into CASPA
8.3 Quantifying indirect albedo effects
8.4 Melt water ponding

9. Running the model in its default form
9.1 Set up BioSNICAR
9.2 Set up automaton
9.3 Run

10 Experiments and Adaptations
10.1 Vertical Migration
10.2 Sudden snowfall events
10.3 dust or BC deposition events

11 TODOs and Development Opportunities
11.1 Bare ice
11.2 Meterological forcing
11.3 Indirect albedo lowering effects DONE
11.4 Model speed
11.5 Edges
11.6 Alternative approaches to bio-optical modelling
11.7 Dust
11.8 Setting initial conditions from aerial imagery

12. Troubleshooting

1. OVERVIEW

This model simulates a snow surface with physical/optical properties defined by the user. This surface is represented as a cellular automaton, i.e. an x,y grid composed of discrete cells that update based upon certain functions as the model advances through time.

There are various modes of operation. The simplest is to simulate an algal bloom that grows from an initial configuration defined by the user. The user defines the % coverage at t=0. At each timestep, algal growth is simulated using a probabalistic function, where growth in situ has a given likelihood, spread of the algae into neighbouring cells has a given likelihood, and spontaneous initiation of a new bloom has a given likelihood. Growth is represented by increasing the cell value - i.e. 0 represents clean ice, 1-10 represent increasing mixing ratio of algae in the upper surface. A carrying capacity is simulated wherein the cell value cannot exceed a value of 10. Once the cell value reaches 10 the bloom can only grow by spreading. If all the neighbouring cells are also at carrying capacity, the algae will not grow.

At each timestep, the grid is thereby updated. The value of each cell is associated with a call to a specific instance of the radiative transfer scheme BioSNICAR. These instances are pre-coded as driver routines saved in the working directory. In this default version, each instance is identical except for the mixing ratio of algae in the upper 3mm of ice. The broadband and spectral albedo of each pixel in the grid is thereby modelled using BioSNICAR and a spatially-integrated albedo computed using a grid-mean. The albedo is used to calculate the radiative forcing following Ganey et al (2017: Nat Geoscience) and Dial et al (2018: FEMS) by multipling the incoming irradiance by 1-albedo for clean and 'mixed' surfaces, the difference between which provides the RF caused by impurities.

One timestep is dimensionless, except that successive SNICAR instances have 2x algal biomass in upper layer, meaning 1 timestep is equal to the doubling time of the algae, making the time dimension tractable. For a doubling time of 3 days, one timestep = 3 days. Albedo change / doubling time (days) = albedo change per day.

Also, in the default version the algal growth is uninterupted, so left long enough the algae will have even coverage at carrying capacity. However, there is the option to interrupt the growth, simulating a rainfall event for example. Could potentially simulate nutrient limitation by increasin or decreasing the doubling times for the blooms. A nutrient nutrient pulse could thereby be simulated.

2. Cellular Automaton

2.1 Initial conditions and update rules

The cellular automaton is a grid composed of equally sized cells that initiate according to a set of initial conditions and then update each time the model iterates (i.e. one timestep) according to a set of rules. Simple automata may update based on the value in an adjacent cell, or an underlying function. In CASPA the underlying cellular model is designed to simulate a snow surface. At t=0 the snow is composed mostly of clean snow with a user defined surface coverage of a second class, which will usually be a low biomass algal inoculant. In the default version of the model, the initial conditions are that the majority of the surface is composed of clean snow and a random selection of cells comprising a total coverage of 0.5% of the entire grid.

At each timestep, cells with algae undergo algal growth. This is represented in the model as a doubling of the algal biomass. This can occur in situ, resulting in a darkening of the same cell, or it can occur by spreading to an adjacent cell. The model simulates this by defining eleven classes of surface:

0 = clean snow
1 = algal biomass 1 (initial inoculant)
2 = algal biomass 2
3 = algal biomass 3
4 = algal biomass 4
5 = algal biomass 5
6 = algal biomass 6
7 = algal biomass 7
8 = algal biomass 8
9 = algal biomass 9
10 = algal biomass 10 (carrying capacity)

At t = 0, 99.5% of the cells in the grid have class = 0, and 0.5% of the cells in the grid have class = 1. Each successive class represents a doubling of the algal biomass, as defined in BioSNICAR (see section 3). Therefore, at each timestep, every cell with class > 0 undergoes growth by one class unit (i.e. biomass doubles). This can occur by that cell increasing by 1 class, or an adjacent cell increasing by 1. The likelihood of each mode of growth can be tuned in the model. The model generates a random number between 1 and 100 each timestep, and the probability of a cell growing in situ or by spreading is set by defining a range of values that the model compares to the randomly generated number. For example, for a 60% chance of in situ growth and 40% chance of growth by spreading, the following logic is applied:

if random number is between 1 and 60: grow in situ
if random number is between 61 and 100: grow by spreading

Growth in situ is achieved simply by increasing the surface class of that cell by 1. Growth by spreading requires an additional decision about which adjacent cell to add biomass to. This is achieved randomly using another random number generator. Every cell has 8 adjacent cells, so a random number between 1 and 8 is generated for that timestep, and each value is associated with a specific neighbour cell. For example:

If the growth is by spreading, rather than in situ:

        generate random number between 1 and 8.

if random number = 1:
add 1 to cell above
if random number = 2:
add 1 to cell diagonally up and right
if random number = 3:
add 1 to cell to the right

Therefore, in this configuration, a timestep causes a doubling of the initial algal biomass, with a 60% chance of growth in situ and a 40% chance of growth by spreading into an adjacent cell. If the growth is by spreading, each neighbouring cell has an equal chance of receiving the additional biomass.

However, there is also an additional rule that simulates the carrying capacity of the snowpack. This is required because algae cannot continue to grow in situ infinitely – there is an upper threshold on the algal abundance that can exist in one location before space and or nutrient availability become limiting. For this reason, we define class value 10 as the upper limit for algal biomass in a cell (i.e. the carrying capacity). If a cell has reached its carrying capacity it can only grow by spreading into neighbouring cells. If the neighbouring cells are also at carrying capacity, the algae in that cell cannot grow. Reaching carrying capacity effectively reduces the probability of growth in situ to zero. Surface class 10 is always associated with algae at carrying capacity as this is hard-coded into the automaton; however the actual carrying capacity is tuneable by defining the algal biomass in BioSNICAR (see section 3) meaning the carrying capacity can be any value. In fact, all of the optical parameters can be tweaked without limit as long as they are divided into ten classes, as this limit is hard coded into the automaton.

Therefore, the automaton updates according to simple rules derived from empirical data about algal growth rates and carrying capacities. The automaton itself updates cell values between 0 and 10, where each value is associated with an instance of BioSNICAR. BioSNICAR is then run with a predefined set of variable values associated with each surface class, returning spectral and broadband albedo outputs. A second grid, identical to the automaton is then populated with those albedo values cell by cell. This ‘albedo grid’ is used for plotting and calculating spatial averages. Each time the automaton updates, the appropriate albedo outputs from BioSNICAR ar eupdated in the ‘albedo grid’.

2.2 CASPA as a Markov Chain

The rules governing the spread of algae over the snowpack can be thought of as a Markov chain, a type of probabilistic cellular automata. A Markov chain is defined by the state of the system at t+1 being dependent only upon the state of the system at t and the likelihood of a transition to another particular state being defined as a probbaility between 0 and 1. An ‘absorbing Markov chain’ includes a defined end-state that, once reachd, the system cannot transition out of. CASPA satisfies these criteria, with some nuance.

There are ten defined states in CASPA (20 in the modified snowfall event scenario) each of which is associated with a specific instance of the radiative transfer model BioSNICAR. A user-generated initial algal coverage defines the probability of a cell being ‘algal’ (i.e. moving from state 0 to state 1) at t=0. For example, with an initial algal coverage of 0.05%, there is a probability of 0.05% that each individual cell has value= 1 at t = 0, and 99.5% chance that each individual cell will have value = 0 at t= 0. The probability that existing algae will grow is then 100%, unless the cell is already at capacity (i.e. cel value = 10), in which case the probability is 0. Probability = 1 within the limits 1-10. There is a crucial additional probabilistic step in that the mode of growth has a probability assigned to it. In the default setup, the algae has a 60% chance of growing in situ, and a 40% chance of growing by spreading into the neighbouring cell. A futher probabilistic model determines the likelihood of each neighbouring cell receiving the growth (by default equal probability for each neighbour). This is also within a limited range, where the cell p can grow in situ only if its algal biomass is below carrying capacity (cell value<10) and the cell receiving the growth can only do so if it exists below carrying capacity (cell value < 10).

This probability network is a Markov chain, because the development of the grid per timestep depends only upon the cell values at the previous timestep, and has no dependence upon the deeper history of the grid. The absorbing state is a cell valie of 10, which cannot be reversed but the cell is also unable to advance further. CASPA also has the option to include sudden step-changes representing snowfall events etc, which adds an important complication to the Markov-chain style evolution of the cellular automaton. In this case, an additional probability (user-defined) defines, at each timestep the likelihood that the system will switch from evolving in 1-unit increments of cell value towards the absorbing state (i.e. algae grows until the grid is covered, given enough time) to an entirely new state (snow covered) where the cell values will sequentially decrease by 1 unit of cell value to a minimum value equal to the original value of the cell prior to the sudden event, after which the original development sequence can continue towards the absorbing state, The attractor-state for the event sequence is the initial value of the cell before the event, but this is not an absorbing state because the cell value will the increase towards the true absirbing state (cell value = 10).

There is great potential for the probabilitis of cell growth, mode of growth and growth direction to be determined by empirical or theoretically-driven models.

2.3 Physical tractability

The evolution of the automaton is governed by the rules described in section 2.1, where algae grow in situ by doubling each timestep up to a carrying capacity. These can be made physically tractable using empirical data from real experiments or from past literature. Since the algae double each timestep, one timestep must be equal to the doubling time of the algae, which is a measurable parameter. The algal doubling time for snow algae has been reported in the literature to be between 3-7 days (REFS). For this reason, the algal doubling time is included in the model as a user-defined variable which is then used to normalise the output data to time in number of days rather than dimensionless timesteps. Further realism is provided by the tuneable parameters in BioSNICAR. The initial inoculum can be set to any value, from infinitesimally low to several parts per thousand which I expect comfortably encompasses the realistic range likely to be encountered in the field.

The carrying capacity of the snowpack is also a measurable property that can be determined using field experiments. It is likely to vary according to geographical location, nutrient supply and local environmental conditions as well as predation and algal community structure (REFS). Therefore, the carrying capacity is user-defined in CASPA. This is achieved (by definition) by setting the biomass mixing ratio in the SNICAR instance associated with surface class 10 (explained further in Section 3).

There is some nuance required in setting the biomass mixing ratios in BioSNICAR which will be discussed in detail in section 3. The tenth class must represent the carrying capacity of the snowpack and each sequential class must double the biomass of the previous, otherwise the model will not be tractable to real time. This means that the choice of biomass in surface class 1 defines the biomass in surface class 10 and vice versa. It is possible to add any number of additional surface classes as long as this convention is maintained; however, this will require updating the main model code to account for the additional classes.

2.3 Edge Effects

Currently a 1 cell sacrificial strip around the grid edges are treated as buckets that cannot update properly because they do not have neighbours to update into. They exist but they are simply ignored by the plotting and grid-mean calculations. There may be options to improve this approach, for example by including an additional condition that if a cell is on the edge it can only spread inwards, or a wrap-around approach where outwards growth connects to cells on the opposite edge. However, these are not implemented in this version.

3. BioSNICAR

incoming irradiance should be the same for snicar runs and for radiative transfer calculations (i.e. same file opened in CASPA code and SNICAR code) so that albedo calculations and IRF calculations are consistent.

4
5
6

7 Biomass, Albedo and Radiative Forcing Calculation

7.1 Biomass

As CASPA progresses through each timestep the algal biomass in a particular cell will increase according to the doubling time (i.e. each timestep the biomass doublesin a particular cell). When this occurs, a uer defined probability determines whether this occurs in situ (i.e. the biomass of that cell increases, the cell darkens) or the algae grow by spreading into one of its neighbours (Moore neighbourhood) chosen at random. A cell’s biomass can only increase while the biomass is less than the carrying capacity (the biomass in the highest surface class). It is therefore possible to calculate at each timestep how many cells have a non-zero biomass, which we define as the algal coverage (Tot_alg_pixels). This can then be expressed as a percentage of the total gridsize (Tot_alg_pixels_percent). However, since there are many classes of non-zero biomass, the coverage is an insufficient description of the biomass on the grid. Therefore, we can calculate the biomass in the grid. For the radiative transfer calculations the impurity load is expressed as a mixing ratio (galgae / gsnow). Since the thickness and density of the upper layer of snow which holds the impurities is known, the mass of snow can be calculated. However, some finite x and y dimension is also required. For this we define a length scale (length_scale) in CASPA which we define as the real-world length of one sid of one cell. Since all the cells are square, we can then calculate the mass of snow in the upper layer of each cell (length^2 * thickness * density). Since impurity load is equal to mass of impurity divided by mass of snow, multiplying the mxing ratio by the mass of snow provides the mass of impurity. In CASPA, the mass of impurity per cell is summed for all cells in each timestep (Tot_biomass) and potted against time (x_time, i.e. timestep * doubling time).

7.2 Albedo

The broadband and spectral albedo are pre-calculated in the CASPA setup routine. SNICAR is run offline to improve the speed of CASPA runs. During setup, the biomass in each surface class is defined and the grain evolution routine run to determine the grain size and layer thickness per layer. This information is then passed to BioSNICAR, which returns a broadband and spectral albedo. These values are then stored in a lookup table which is accessed by CASPA by indexing to the pertinent row and columns according to the surface class of a particular cell. The spectral and broadband albedo of the entire grid are calculated using a simple 2-D mean.

7.3 Radiative Forcing
Radiative forcing is calculated per cell, per timestep using a spectral differencing method (cf Ganey et al., 2017). At each timestep, the spectral albedo of each cell is inverted (1 – albedo) because albedo is a measure of energy not absorbed by the snow – for radiative forcingwe are interested in the amount of energy absorbed and made available for raising the temperature or melting ice. The inverted albedo for clean and algal snow is multiplied by the incoming spectral irradiance (variable name ‘incoming’) which is obtained from a text file that can be a SNICAR default or a user-provided measured/simulated incoming spectrum. Since the incoming spectral irradiance is in units of Wm-2, incoming multiplied by inverted albedo provide the energy absorbed in the snow in Wm-2. This is achieved using the following code in CASPA:

Alb_inv = 1.-spectral_average;
Alb_inv_clean = 1.-snicar_clean_spectral;
IRF_spectral = alb_inv.*incoming;
IRF_clean = alb_inv_clean.*incoming;
IRF_BBA = sum(IRF_spectral);
IRF_BBA_clean = sum(IRF__clean);

Where alb_inv is 1-albedo, IRF_spectral is the energy absorbed at each unit wavelength, and IRF_BBA is the energy absorbed across the entire solar spectrum. These are referred to as IRF or instantaneous radiative forcing because they are not integrated over time. Since the incoming irradiance is a flux with units Wm-2 where 1 Watt is equal to 1 joule per second, the IRF is the flux over the area of the grid in one second. Our temporal resolution is equal to the selected doubling time, meaning we assume the IRF to be constant within a timestep.

The instantaneous radiative forcings (/s) are converted into radiative forcing over the whole timestep. This is achieved by multiplying by 24 (hours per day) then by 60 (minutes per hour) and by 60 again (seconds per minute). This provides radiative forcing over the grid in one day. To calculate the radiative forcing over the timestep, the daily radiative forcing is multiplied by the doubling time (unit= days). The radiative forcing over the entire area over the timestep due to algal cells can then be calculated as the difference between the total radiative forcing for algal snow and the total radiative forcing for clean snow. The CASPA code for achieving this is:

%%% IRF calculations integrated over wavelength and time

% NOTE that the IRF here is measured per second by default. This is
% because the radiative transfer equations are calculations of flux,
% where flux is energy per unit time measured in Watts, where 1 watt =
% 1 joule/second.

RF_BBA = sum(IRF_BBA.*24*60*60); % total RF over area over entire time of model run
RF_BBA_clean = sum(IRF_BBA_clean.*24*60*60); % total RF over area over entire time of model run
RF_BBA_impurities = RF_BBA - RF_BBA_clean; % total RF due to impurities over entire area over entire area and time of model run

% daily RF (average daily RF - not calculated for individual days, but calculated by dividing total by no. of days)
RF_daily = RF_BBA/doubling_time; % RF for whole area per day
RF_daily_clean = RF_BBA_clean/ doubling_time; % RF for whole area per day, clean snow
RF_daily_impurities = RF_BBA_impurities / doubling_time; % broadband RF for whole area due to impurities, per day

% daily, per metre (again, calculated as average over space and time
% divided by gridsize and number of days)

RF_daily_per_m = RF_daily / gridsize; % assuming 1 cell is 1 x 1 m
RF_daily_clean_per_m = RF_daily_clean / gridsize; % assuming 1 cell is 1 x 1m
RF_daily_impurities_per_m = RF_daily_impurities / gridsize; % assuming 1 cell is 1 x 1 m

The albedo and IRF is plotted in Figure 2. This shows the instantaneous radiative forcing over the entire grid at each timestep – it is not integrated over time.

8 Snow grain evolution

8.1 Grain growth parameterisation

Snow grain evolution is incoporated into CASPA using the parameterisation proposed by Flanner and Zender (2006) and Kuipers-Munekke et al. (2011), updated to simulation the development of the effective radius (reff) of the snow grains rather than the specific surface area (SSA). This is because small errors in low SSA values produced large variations in reff because the two are inversely related. This is also the parameterisation that simulates grain growth in the Community land Model (CLM). Details of the parametrisation and its integration into CLM are available at http://www.cesm.ucar.edu/models/cesm1.0/clm/CLM4_Tech_Note.pdf. Grains are still assumed to be speres, as per SNICAR, which has previously been shown to result in small errors in hemispheric flux simulations (e.g. Grenfell and Warren, 1999).

The rate of change of grain size is calculated as the sum of the rates of change due to wet growth, dry growth and refreezing. Wet growth refers to grain growth by the presence of liquid water in the snowpack. Liquid water droplets themselves do not significantly alter the snowpack albedo because the refrcative indices of water and ice are very similar across the solar spectrum; however, interstitial ponded water is important as it replaces air-ice interfaces where high angle scattering can occur with ice-water interfaces where scattering is more likely in the forward direction. Liquid water can coarsen snow grains (Brun et al., 1989) and can refreeze into large droplets. These processes are accounted for in the parameterisation as wet (re,wet) and refreezing (re,ref) growth.

The parameterisation relies upon several constants. We assume that the effective radius of refrozen water is always 1500 microns, and that fresh snowfall has an effectove radius of 100 microns. The dry snow aging calculation is based upon a parameterisation of a model proposed by Flanner and Zender (2006) which accoutns for vapour diffusion between ice crystals. This model relies upon inpout values for temperature gradient, snow temperature and effective radius of each vertical layer in the snowpack. These values are retrieved from SNICAR and used to retieve apropriate empirical parameters from a lookup table provided by Flanner and Zender (2006). In this model, maximum grain growth occurs when the snow is warm, the temperature gradient is high and the snow has low density. The lookup table includes values ranging from 223-273K for snow temperature, 0 – 300Km-1 for temperature gradent, 50 – 400 kgm-3 for snow density.

The effects of liquid water are modelled according to a parameterisation proposed by Brun et al. (1989). This depends upon the liquid water fraction, which is uder defined in CASPA. There is a constant term, C, with a value of 4.22x 10-13. Refreezing is simply calculated as the product of the effective radius of refrozen ice (assumed to be 1500 microns) and its fractional abundance in the snow layer (0-1). The net change in grain radius is then calculated as the sum of the growth due to wet, dry and refreezing.

The fraction of liquid water produced in each layer during each timestep is calculated using the excess energy above the frezing point and the latent heat of fusion for ice (Lf). The excess heat is calculated as the residual between the temperature and the temperature at freezing point (273.15 K). This is converted into excess energy using the equation

E_excess = T_excess * dz(i) * c

where c is the volumetri heat capacity of the layer, calculated as:

c = (mass_wat(i) / dz(i) * CWAT) + (mass_ice(i) / dz(i) * CICE)

where mass_wat(i) and mass_ice(i) are the masses of ice and water per layer, calculated as layer thickness multiplied by density, CICE and CWAT are the specific heat capacities of ice and water (constants) and dz(i) is the thickness of the layer.
The mass change resulting from the ecess energy is equal to the excess energy in the layer divided by the latent heat of fusion for ice. This mass change is then added to the liquid water mass and subtracted from the solid ice mass. The new liquid water fraction is calculated as the ratio of water to ice. The code for this is:

for i = 1:1:nbr_lyr % iterate through each vertical layer
    % assign input values
    density = rho_snw(i);
    r0 = r0;
    r = rds_snw(i);
    temp = T(i);
    TG = temp_grad;
    doubling_time = doubling_time; % required to convert timestep into days
    fliq = fliqs(i); % assign liquid water fraction
    f_ref = f_refs(i);
    r_new = grain_size_evolution(temp,TG,density,r0,r,doubling_time,fliq,f_ref); % function call from grain_size_evolution.m
    new_r(i) = r_new; % append new radius into array

        if T(i) >= 273.15 % if layer temp is greater than freezing point, initiate melting code to update liquid water fraction per layer...

        T_excess = T(i) - 273.15; % calculate residual T that could be used for melting
        mass_ice(i) = dz(i) * rho_snw(i); % mass of ice = layer thickness * density
        mass_wat(i) = ((mass_ice(i)/917)*1000) * fliqs(i); % mass of water = (mass of ice converted to mass of water, multiplied by liquid water fraction)
        c = (mass_wat(i) / dz(i) * CWAT) + (mass_ice(i) / dz(i) * CICE); % c is the volumetric snow/soil heat capacity (J m-3 K-1)
        E_excess(i) = dz(i) * T_excess * c; % excess energy = excess heat (K) * layer thickness (m) * specific heat capacity of snow (J/m3/K) (OVER TIMESTEP)
        W_change(i) = E_excess(i) / Lf; % change in water mass = excess energy / energy required to melt ice (latent heat of fusion)
        new_W_mass(i) = mass_wat(i) + W_change(i); % updated water mass = old + change
        new_I_mass(i) = i_mass(i) - W_change(i); % ice converted to water, so subtract change in water mass from initial ice mass
        new_fliqs(i) = new_W_mass(i) / new_I_mass(i); % new liquid water fraction
        % using this scheme assumes all excess energy is dissipated in
        % phase change ice -> water. Amount of excess energy determines
        % mass of water produced
        end
end

This is a simplified version of what is used in CLM (see CLM technical document pg 110). Note that I have added a few nuances to this scheme when implementing in CASPA. There is a loop in the snicar_driver_heating.m script that percolates newly formed liquid water down through the snowpack such that there can never be more liquid water in higher layers than lower layers in the snowpack. If this situation arises (as it does almost always due to melting in the upper layers) a residual water film can be maintained in the upper layer using the coated sphere approach explained in section 8.4 but the liquid water fraction bounces down the the snow layers to accumulate from the bottom up. There are two important parameters controlling this – perc_threshold and fliq_max. The first is the threshold liquid water fraction that needs to exist on a snow layer for percolation to start (i.e. for perc_threshold = 0.01, if there is less than 1% liquid water in the layer, the liquid water can stay in the layer without percolating down to a lower layer). The second is the maximum liquid water fraction that can exist in a water layer before water simply piles up in the overlying layer (i.e., for fliq_max = 0.2, if 20% water fraction exists in the bottom layer, percolation will accumulate water in the second-to-bottom layer insead, until that too reaches 20% liquid water fraction). These values are user defined. Since this all occurs within the calculations for each timestep, the user will never see the water generate in the upper layer and percolate down, the model will simply report the additional water in the lower layer. It is important to remember that since liquid water ponding is not accounted for in this model, what is accumulating in the bottom layer is the grain-rounding effect of liquid water (as in CLM), rather than water itself. Liquid water in each layer will therefore percolate to lower layers. Then, if the temperature is below the freezing point, this liquid water will become refrozen water.
At the end of the timestep, the code checks to see if liquid water is present in any layers where the temperature is below freezing (273.15 K). If so, this liquid water fraction is converted into refrozen water,. It is therefore removed from the variable ‘fliqs’ and added to the variable ‘f_refs’.

The code for this (where nbr_lyr is the number of vertical layers in the snowpack, and new_fliqs is the liquid water fraction in each layer at the end of the timestep) is as follows:

% The following loop percolates new liquid water down through the snowpack.
% Regardless of the layer the water forms in, it will immediately percolate
% to the bottom, then accumulate from bottom up. There is a percolation
% threshold. If the liquid water fraction exceeds that threshold, liquid
% water percolates downwards, provided the layer beneath its max capacity
% (fliq_max).

for i = 1:1:nbr_lyr-1
    % if higher layer contains more water than lower layer, higher layer exceeds percolation threshols and lower layer is not at max liquid water fraction-
    % percolate down
    if new_fliqs(i) > new_fliqs(i+1) && new_fliqs(i) > perc_threshold && new_fliqs(i+1) < fliq_max
        c = new_fliqs(i)-new_fliqs(i+1)-perc_threshold; % c = difference in water fractions between upper and lower layer
        new_fliqs(i+1) = new_fliqs(i+1)+c; % add difference to lower layer
        new_fliqs(i) = new_fliqs(i)-c; % remove difference from higher layer
    end
end

% At the end of the timestep, check whether liquid water exists in layers where temp is below freezing.
% If so, turn this liquid water fraction into refrozen fraction. Raise
% warnings if liquid and refrozen fractions together exceed 1, and also
% raise a flag if the user should include a liquid water film in the next
% timestep.

for i = 1:1:nbr_lyr
    if new_fliqs(i) < 0
        new_fliqs(i) = 0; % if new < old, it can't have -ve water, so reset to zero.
    end

    if new_fliqs(i) > 0 && T(i) < 273.15
        new_f_refs(i) = f_refs(i) + new_fliqs(i);
        new_fliqs(i) = 0;
    end

    if new_fliqs(i) > 0
        ADD_WATER = "LAYER " + num2str(i) + " melting: add liquid water film" % Alert user to add water film b/c ice is melting
    end
end

It is important to note that there is an element of arbitrariness to some of the variable value assignments since we lack empirical observations to determine the initial fractions of liquid water, fliq_max, perc-threshold, fraction of refrozen ice and initial temperature gradient. However, these are all measurable in the field and although they are just estimates in the default release, they can be updated according to real field experiments by individual users ad hoc.

The code also calculates the mass of each snow layer. Since the mass, density and volume of the snow layer are related by the equation mass = volume * density, we can use the updated mass to estimate the new layer thickness by assuming the density remains constant. This is justified by considering two possibilities for snow melting: either it can erode in situ and become less dense, or it can maintain its density and get thinner as it loses mass. By defining the layer density as constant, the layer thickness can evolve as the snow melts. The updated layer thickness is then provided in the input table. This also incorporates within it an emergent scavenging estimation, since the impurities are gradually distributed over a smaller and smaller volume. Tyhe new layer mass is updated by taking the original ice mass and multiplying by 1 + refrozen fraction and 1 – liquid water fraction, to account for ice added by refreezing and lost by melting:

new_i_mass(i) = i_mass(i) * (1 + new_f_refs(i)) * (1 - new_fliqs(i)); % calculate mass of each layer (inc those below freezing) after percolation)

    new_dz(i) = new_i_mass(i) /rho_snw(i); % update layer thickness

ISSUE: Bottom layer grows in thckness instead of density due to accumulation
ISSUE: Faults for an isothermal snowpack

The code also checks to make sure the layer thickness is not thinner than the effective radius in that layer.

The code therefore accounts for dry and wet snow grain evolution, but to account for water and refrozen water in the instances of SNICAR called by CASPA, the effective radius of the grains must be amended to take these factors into account. This is achieved by assuming refrozen water has an effective radius of 1500 um (consistent with CLM). The final effective radius for each snow layer is the weighted average of the radius of the snow grains and the refrozen water. The radius of a water coating to be added to the snow grains is calculated by multiplying the final grain effective radius by the liquid water fraction (e.g. if the grain is 100 microns and the liquid water fraction is 0.1, the code will recommend adding a 10 micron water coating). The precise optical properties for the grains will need to be added to the BioSNICAR library using the Mie codes provided.

These values are all provided in a single table when the setup code is run (see section 9.1).

8.2 Incorporation into CASPA

The parameterisation detailed in 8.1 is implemented into CASPA via amendments to the SNICAr driver routine and a bespoke function in a separate script (grain_size_evolution.m). In the initial release, a degree of manual operation is required to integrate the grain growth calculation into the main CASPA model. This is because the grain growth section of the SNICAR returns a column vector of updated grain sizes for each layer of the snowpack which then needs to be manually entered into the next instance of SNICAR as the initial grain radii. To clarify:

at t = 0:
rds_snw = [100 200 200 300 500] % initial grain radii

output = new_r [130, 240, 245, 367, 559]

at t = 1:
rds_snw = [130 240 245 367 559] % manually input from t = 0 new_r

output = new_r [155 256 299 375 600]

at t = 2:
rds_snw = [155 256 299 375 600] % manually entered from t=1 new_r

output = new_r [200 300 346 401 620]

etc...

This means each instance of SNICAR saved in the working directory should already have updated grain sizes before the cellular model is run. The grain sizes are set prior to running the cellular model, and they update in CASPA by calling the relevant instances of SNICAR, precisely as for the algal biomass. This approch has advantages and disadvantages – it is good for computational efficiency and tractability of the main CASPA scheme, but the cost is increased set up time and less automation.

The grain size evolution code is run simply by running the SNICAR driver routine ‘snicar_driver_heating.m’ which includes set up and calls to the grain growth script, which must also be saved in the working directory (grain_size_evolution.m). This separate script requires access to a lookup table (drdt0_bst_fit_60.mat). The code works by first reading in the user defined variables from SNICAR. These are:

temp: snow temperature (calculated automatically from heating rates and initial temperatures defined in SNICAR)

TG: temperature gradient (calculated automatically in SNICAR)

density: defined in SNICAR input

r0: effective radius of fresh snow, assumed to be 100 microns

r: current effectve radius, defined in SNICAR input

doubling_time: doubling_time for algal blooms – required to turn dimensionless timestes into days, must be cinsistent with the doubling time defined in CASPA (default = 3d)

fliq: fraction of liquid water present. Retrieved from user defined array ‘fliqs’

f_ref: fraction of refrozen water: Retrieves from user defined array ‘f_reqs’

These values are then used in the call to the function ‘snow_grain_evolution’. This function takes the user defined variables, along with the model constants and uses them to apply the grain growth parameterisation described in 8.1. The values of T, TG and snow density are used to retrieve values fr three empirical parameters, kappa, tau and drdt0, stored in the lookup table ‘drdt_bst_fit_60.mat’. The rate of grain growth is provided per hour, and is then multiplied by 24 to provide grain growth per day. Since one timestep is often > 1 day, according to the doubling time, the daily grain growth is multiplied by the doubling time to quantify the grain growth per timestep of the CASPA model. This resultant grain growth value is added to the initial grain growth at each timestep to provide a new grain size to be input to the next instance of SNICAR. Once the user has repeated this process and saved each instance as a sequentially numbered version of SNICAR in the working directory, CASPA should be able to call n instances of SNICAR, each one with sequentially updated grain sizes (and, optionally, impurity concentrations etc).

8.3 Quantifying indirect albedo effects

It is also possible to quantify the direct and indirect effects of an impurity by creating two sets of SNICAR instances – one set with the grain growth model turned on, one set with the grain growth model turned off. The difference in albedo between the two sets is equal to the simulated indirect albedo reducing effects.

8.4 Meltwater ponding
Melt water ponding is dealt with simplistically in this model, and can only be accounted for grain growth or coating ice grains with water layers. Therefore, this model is limited to modelling snowpacks that are fairly well-drained at the surface and water does not fill interstitial spaces. Water in the snowpack is a variable driving the grain growth model (see Section 8.1) and can lead to grain growth by refreezing. Where liquid water is present and the temperature is above freezing (273.15K) the water is generated proportionally to the mass of ice lost as a result of excess heat in the snow layer. Some of this water will percolate down through the snowpack if the water fraction exceeds a threshold and the lower layers have capacity to accept water input, leaving behind a residual water coating in the origin layer. Assuming the water in layer dz is either at or below the percolation threshold, the thickness of water coating is calculated using the mass of water and mass of ice present within the layer. A water coating value is thereby added to the output table for each layer in each run. This is achieved in the setup code and automatically calculates the Mie optical properties for grains of the precise size and thickness of water coating generated by the grain size evolution model and adds them to the BioSNICAR lookup library.

Meltwater ponding is dealt with very simplistically in this model. There is an IF statement in the driver script that prints an instruction to add a liquid water layer to the grains added to the next instance of SNICAR whenever the ice temperature exceeds 273.15 K (OC, melting point). This means that in many cases new optical properties will need to be calculated for the specific ice-water combination required for the next instance of SNICAR. This requires applying the script ‘mie_coated_driver’ and specifying the ice grain radius (obtained for each layer from r_new) and an outer coating of liquid water. The code will require the refractive indices for ice and water (Warren., 2008 and Segelstein, 1981) to be available in the working directory. This will output into the workspace all the relevant optical parameters for that ice-water configuration. The new ice-water grains will then need to be added to the SNICAR library as a NetCDF file. This can be achieved using the script ‘NetCDF_Updater’, which will automatically create the file in the right format provided the mie-driver has been run immediately befoe so that the optical parameters are stored in the workspace. The naming convention for the ice-water files is a little esoteric, as a legacy effect of the incorporating water films into the original SNICAR code by joining strings for grain and film diameters. The files should be named as follows in order to be readable by SNICAR:

ice_coated_wrn_234_50.nc

where “ice_coated” indicates that there are two concentric layers to the grain – ice core and water film. “_wrn_” refers to the choice of refractve index used – in this case Warren (2008). “_234_” is the effective radius of the ice grain in microns (obtained from r_new for each layer). “_50.nc” is the thickness of the water film coating the ice grain in microns, plus the file extension.

If coated spheres are used in the model, there is a small modification that should be made when inputting the grain sizes into the SNICAr driver. For the layer where liquid water is present, a zero should be input in the variable rds_snw. The ice-water radius should be added to the rds_coated variable instead. This is achieved by adding the numerical part of the filename. For example, for a 200 micron ice grain coated with a 50 micron liquid film is input in the upper two layers, over three layers without water ponding would be input as follows:

filename = ice_coated_wrn_200_50.nc

In SNICAR:

rds_snw = [0, 0, 245, 367, 559];
rds_coated = [“200_50”, “200_50”, “0” “0” “0”];

Note that in this release the coated grains are input as strings whereas the non-coated grains are input as numbers. This is because two separate numbers are required for the coated grains and to use the num2str or int2str function in matlab these numbers would have to be concatenated without the separating underscore. In many cases this would lead to confusion about the grain size (e.g. 200 micron grain + 20 micron water would be concatenated into 20020) and it might not always be clear in the file name which part refers to the ice and water.

9.1 Setting up BioSNICAR

To run CASPA, an instance of BioSNICAR must exist in the workspace associated with each possible surface class. Each of these instances is run at the beginning of the CASPA run and the outputs stores in the workspace, rather than calling BioSNICAR from each cell (i.e. for 10 surface classes in a 100 x 100 cell grid, this method calls BioSNICAR 10 times instead of 10,000 times). The inputs to each instance of BioSNICAR are set depending upon whether the user wnts to incorporate a grain size evolution model or not. If not, ten identical instances of BioSNICAR can be saved in the workspace, then the biological impurity mixing ratio updated in each manually. If the grain size evolution model is incorporated, there are several setup scripts which output a csv file containing the relevant input prameters to insert into each instance of BioSNICAR. These setup codes use the full BioSNICAR code adapted to incorporate the grain size evolution protocol described in section 8, but reconfigured as a function rather than a standalone script and named “snicar_melting_setup.m”. This function is called by the driver script “snicar_setup_melting_driver.m”. This driver has initial conditions set by the user, and returns updated values for all the relevant inputs for the next run calculated from the grain size evolution code (section 8). This provides the user with a csv file containing the inpout parameters that should be set in each instance of BioSNICAR to be read into CASPA. The user then has to do this manually. Then, a run of CASPA will incorporate both algal growth and grain evolution. Note that the output table contains the following variables for each snow layer, for each SNICAR instance:

r = effective radius (i.e. rds_snw in SNICAR). This is the radius taking into account refrozen water in the layer.
w_coat = thickness of water coating to be applied to the grains
x = biological impurity mixing ratio

        x r_top r_z2 r_z3 r_z4 r_btm w_coat_top wat_coat_z2 wat_coat_z3 wat_coat_z4 wat_coat_btm
        ________ _____ ____ ____ ____ _____ __________ ___________ ___________ ___________ ____________

    SNICAR_INIT 0 100 100 150 200 250 0 0 0 0 0
    SNICAR_1 10000 843 715 311 207 272 22.469 9.7127 3.1072 0 0
    SNICAR_2 20000 884 744 373 214 301 74.852 24.127 3.7321 0 0
    SNICAR_3 40000 923 772 425 221 332 78.712 25.726 4.25 0 0
    SNICAR_4 80000 961 800 471 228 367 82.094 27.047 4.7102 0 0
    SNICAR_5 1.6e+05 999 828 515 236 416 84.808 28.064 5.1515 0 0
    SNICAR_6 3.2e+05 1036 855 556 244 589 85.763 28.451 5.557 0 0
    SNICAR_7 6.4e+05 1074 882 596 252 598 0 27.773 5.959 0 0
    SNICAR_8 1.28e+06 1112 910 635 260 607 0 25.657 6.3523 0 0
    SNICAR_9 2.56e+06 1153 939 675 269 616 0 21.883 6.7529 0 0
    SNICAR_10 5.12e+06 1194 968 715 278 626 0 17.141 7.1469 0 0

 Table X:example output table from the CASPA set up code.

The script then automatically calls a mie solver and automatically calculates the mie optical properties of the ice grains included in the CASPA setup file (table above) including water coatings, and adds these as netCDF files to the BioSNICAR lookup library. Therefore, no further steps are required after running the setup codes except for using the data in the output table to populate 10 instances of SNICAR. The list of biomass misxing ratios in each instance is also saved to the workspace as ‘Biomass.mat’ which is then used in CASPA to calculate the total biomass of the grid.

11 Troubleshooting

1. If the liquid water fractiosn are greater in higher than lower layers
Check the refrozen layers. Water can percolate to the bottom then refreeze if the temperature is low enough. In this case, that water will disappear from the fliqs variable and instead be represented in the f_refs variable. At first glance this may seem like the percolation code is broken.

Model limitations:

model instability with extreme biomass

TODOS

1. Deal with edge effects (-1s and +1s can push the indexing out of grid
range, currently counter starts at 2 and ends at i,j -1, but this
leads to a border that doesn't update) and simply isn't plotted.

2. Could add an additional randi() dice roll to randomly reduce value
of cells, simulating rainfall washaway. Alternatively, a sudden dust
deposition event...? These don't have to be random, they could start
on a particular ticker value (e.g. at 20th timestep: rain).

3. Can the initial grid be set using UAV por satellite imagery?

4. How should I deal with dust? constant background?

VERSION 4 EDITS:

1) Updated colormap to show clean snow as white, then grades of red

2) Radiative forcing calculations: ***** add details here *****

3) Some minor edits to variables names etc for readability

%%% USER DEFINED VARIABLES: SET HERE %%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%

%read incoming irradiance file and assign to variable 'incoming'
fileID = fopen('media/joe/9446-2970/FromGardner/snicar_package/mlw_sfc_flx_frc_clr.txt');
incoming=textscan(fileID,'%f','Delimiter',',');
incoming=cell2mat(incoming); %convert to column vector
fclose(fileID);

% set up time ticker (time_tot = total no of timesteps in run)
time_tot = 28;
timestep = 1;

% %% Set up grid
gridsize = 10000; % total grid area (no. cells)
gridx = 100; % length of x-axis
gridy= 100; % length of y-axis
alg_frac = 0.5; % percentage of algal coverage at start of experiment (all initialise as light algae: class 1)
non_alg_frac = gridsize-alg_frac; % residual = non-algal, assumed clean
doubling_time = 3; % algal doubling time in days (3 is fast, 7 is slow - from literature e.g. Yallop, Stibal)